# SSH Configuration
The following changes need to be made for SSH:
User Group to control access
Create Group “remotessh”,
Add users that are allowed remote access to the group.
In file /etc/ssh/sshd_config
add the following lines to bottom of file:
#
# Westrick GmbH Configuration
#
Port	26
AllowGroups	remotessh
GatewayPorts	yes
X11DisplayOffset	50
X11Forwarding	yes

restart ssh server with: “rcsshd restart”
In file /etc/ssh/ssh_config
Add lines:
ForwardAgent	yes
ForwardX11	yes

Then for each known host with alternate port add following lines before “Host *” line:
Host	jerry.westrick.com
  Port 26

# Setup NxServer
Install the nxserver software with yast.
Execute following command in root-shell
nxsetup --install --setup-nomachine-key

Edit /etc/nxserver/node.conf:
change port to 26
SSHD_PORT=26

Enable SSH Authentication
ENABLE_SSH_AUTHENTICATION=”1”

Add user nx to remotessh group!

Download nxclient from http://www.nomachine.com/download.php .
When connecting you need to specify 2 options:
1. General->Server->Port is 26.
2. Advanced->Network->Enable SSL encryption of all traffic is enabled.

Open port 26 in Firewall!